## Slide 1
INTERNET OF THINGS HARDWARE

## Slide 2: CONTENT OUTLINE
Microcontrollers vs. Computers
Good for sensors Good for sensors and processing Good for processing and network Ethernet vs. ESP8266 -01 Introduction: Esp8266 node-MCU
Esp8266: Pinouts

## Slide 3: MICROCONTROLLER vs. COMPUTERS
Simple Build Systems Control hardware Low speeds
Small memory
GPIO PWM ADC
Run single software (Bootloader)

## Slide 4: MICROCONTROLLER vs. COMPUTERS
Embedded CPUs
High Ram High Speed
Large Memory with extendable size Modest in controlling hardware GPIO
Run on OS
No real time execution

## Slide 5
I.
GOOD FOR THE SENSORS
ARDUINO
ATMega 328P
ChipKIT
PIC Controller
LaunchPad
MSP430

## Slide 6: II.
GOOD FOR SENSORS
& PROCESSING
STM32
STM Nucleo
ARM Cortex M
ESP8266 node-MCU
Espressif ESP8266
WiFi Module
ESPRUINO
ARM
Javascript

## Slide 7
III.
GOOD FOR PROCESSING
& NETWORK
Raspberry PI CPU Module 900MHz ARM
OS Environment 1 GB RAM
Intel-Galileo
400 MHz Quark x86
256 MB RAM
Intel Edision
1GHz Dual Core Atom X86
WiFi, 4GB Flash

## Slide 8: ESP8266 Wi-Fi vs.
ETHERNET MODULE
Small programmable device
Easily connectable
Open source
Has a simple to use software Only around four simultaneous networking connections

## Slide 9: ESP8266 Wi-Fi vs.
ETHERNET MODULE
802.11 b/g/n
Wi-Fi Direct (P2P), soft-AP Integrated TCP/IP protocol stack Programmable GPIO
1MB Flash Memory
Integrated low power 32-bit CPU could be used as application processor SPI, UART

## Slide 10: ESP8266 -01

## Slide 11: INTRODUCTION: ESP8266 - 01
An open-source firmware and development kit that helps you to prototype your IOT product within a few Lua/C++ script lines.
Arduino-like hardware IO
Node-JS style network API
Lowest cost WI-FI

## Slide 12: INTRODUCTION: ESP8266 - 01

## Slide 13: Esp8266 - 01 PINOUTS
2 Digital Pinouts: GPIO1 GPIO2
USART: RXD TXD
Power Supply VCC – 3.3V CH_PD – 3.3V GND
Programming via Rx-Tx FTDI USB

## Slide 14
THE THING
ARDUINO MEGA

## Slide 15: INTRODUCTION: ARDUINO
ARDUINO is an open-source Electronics Prototyping Platform based on easy – to – use hardware & software. It’s intended for anyone making interactive projects.

## Slide 16: ARDUINO ECOSYSTEM
COMMUNITY
SOFTWARE
BOARD

## Slide 17: ARDUINO FLAVOURS

## Slide 18
ARDUINO MEGA MICROCONTROLLER

## Slide 22: INTRODUCTION: ATMEGA 2560
Atmel ATMega 2560 is the heart of MEGA version Arduino.
This TQFP microcontroller features 16 MIPS throughput
capability at 16MHz CRYSTAL.
I/O :
  Digital Ports: Total 54 I/O Pins.
ADC Pins : A0 to A15
USART: PD0 (RXD) PD1(TXD)
PWM: 15 out of 54 Digital I/O can be used as PWM outputs
Power: Chip operates in between 1.8V to 5.5V

## Slide 23: ARDUINO MEMORY
FLASH:
In system reprogrammable non-volatile program space storage is 256KB.
A separate memory space partitioned for Boot Flash section
of 8KB.
SRAM:
Temporary values, stack of volatile type memory, memory size 8KB
EEPROM:
4KB of space availability storage space for long-term.

## Slide 24: ATMEGA 2560
FEATURES
TIMER:
Two 8-bit Timer/Counters with Separate Prescaler and Compare Mode Four 16-bit Timer/Counter with Separate Prescaler, Compare- and Capture Mode
PWM:
Four 8-bit PWM Channels
Twelve PWM Channels with Programmable Resolution from 2 to 16 Bits
USART:
Four Programmable Serial USART
ADC:
16-channel, 10-bit ADC

## Slide 25: ARDUINO: PIN DIAGRAM

## Slide 26: HAPPY LEARNING…

## Slide 27: THANK YOU